## Slide 1: Green Communities
Criterion 5

## Slide 2: Criterion 5
Establish requirements to minimize life-cycle energy costs for new construction (suggested route for achieving this step is via adoption of "Stretch Code“)

## Slide 3: Criterion 5 Minimize Life-Cycle Costs
A municipality must require all new residential construction and all new commercial and industrial real estate construction to minimize, to the extent feasible, the life cycle cost of facilities/buildings by utilizing energy efficiency, water conservation and other renewable or alternative energy technologies.
The recommended way for cities and towns to meet this requirement is by adopting the Board of Building Regulations and Standards (BBRS) Stretch Code (780 CMR 115.AA), an appendix to the MA State Building Code. If your municipality adopts the Stretch Code. All new residential construction, irrespective of size/square footage, will be subject to the Stretch Code.
Towns are advised to adopt the Stretch Code as a general bylaw at Town Meeting.

## Slide 4
Modeling Analysis: Single Family Natural Gas or Propane Heated Home:
2,550 sq. ft., 3 bedroom
FEATURE Base Code Stretch Code Construct
Cost
HERS RATING 66 55 $500
WINDOW (U-VAL/SHGC) .30/.30 .27/.30 $500
HEATING 92% gas furn 96% gas furn $290
COOLING 13 SEER 15 SEER $392
DHW 0.62 EF 40 Gal tnk Gas 0.96 EF Tnklss Gas $724
DHW 0.62 EF 40 Gal tnk Prpn 0.94 EF Tnklss Prpn
DUCT LEAKAGE 4 CFM25 / 100 CFA 2 CFM25 / 100 CFA $200
HIGH EFF LIGHTING 100% CFL No change required $0
AIR INFILTRATION 3.0 ACH50 No change required $0
FOUNDATION Uncnd, uninsul bsmnt No change required $0
FLOOR R38 fbrglss Grade 1 No change required $0
WALLS R21 fbrglss Grade 1 No change required $0
CEILING – FLAT R-50 blown in cellulose No change required $0 TOTAL $2,606

## Slide 5
9th Edition Stretch Code Modeling Analysis 2550 sq.ft. 3 BR Single Family Home w/ Oil Heat
Feature Base Code Stretch Code Const. Cost
HERS RATING 70 54 $500
WINDOW (UVAL/SHGC) .30/.30 .27/.30 $500
HEATING 83% oil furnace 96% oil furnace $1,759
COOLING 13 SEER 15 SEER $392
DHW 0.95EF Tnk Elect 3.24EF Heat Pump DHW $660
DUCT LEAKAGE TO OUTSIDE 4 CFM25/100 CFA 2 CFM25/100 CFA $200
FOUNDATION Uncond, uninsul bsmnt No change required $0
FLOOR R38 fiberglass Grade 1 No change required $0
WALLS R21 fiberglass Grade 1 No change required $0
HIGH EFF LIGHT 100% CFL No change required $0
CEILING – FLAT R-50 blown in cellulose No change required $0
DUCT INSULATION R-8 No change required $0
TOTAL $4,011

## Slide 6
Criterion 5 recommends that municipalities minimize the life-cycle cost of all newly constructed homes and buildings, as well as those undergoing major renovation, by adopting Massachusetts’ Board of Building Regulations and Standards (BBRS) Stretch Code (780 CMR 115.AA). Buildings constructed to the Stretch Code use significantly less energy than buildings built to other current and previous building codes.

## Slide 7
Costs and benefits to meet stretch code
Single Family Gas Heated Home
HERS Index (ERI)
Target 55
Example Base 66
Example Stretch 55
COSTS BENEFITS NET
BUILDER
Adjustments Utility Cost
+ HERS Rater Fee Rebates1 Compared to Base Code
+$(2,606) -$1,630 $(976)
HOMEBUYER
Chng Chng Est Red Year 1 Year 2+
to to Annl Energy Csh Flw Cash Flw
Dwnpymnt³ Mrtgg Pymnt³ Cost/Year²
+$(97) +$(77) -$213 $37 $135

## Slide 8
Single Family Home with Propane Heat
COSTS BENEFITS NET
BUILDER
Adjustments Utility Rebates1 Cost
+ HERS Rater Fee Compare to Base Code
+$(2,606) -$1,626 $(980)
HOMEBUYER
Chng to Chng to Est Reduc d Yr 1 Yr 2+
Dwnpymnt³ Annual Energy Cash Cash
Mortgage Cost /Yr² Flow Flow
Pymnt³
+$(98) +$(77) - $475 $299 $397

## Slide 9
9th Edition Stretch Code Modeling Analysis 2550 sq.ft. 3 BR Single Family Home with Oil Heat
HERS Index (ERI)
Target 55
Example Base 70
Example Stretch 54
Costs and Benefits to Meet Stretch Code
COSTS BENEFITS NET
BUILDER
Adjustments Utility Rebates1 Cost Compared
+ HERS Rater Fee to Base Code
+$(4,011) -$1,593 $(2,418)
HOMEBUYER
Change to Change to Estimated Year 1 Year 2+
Downpayment³ Annual Reduced Energy Cash Cash
Mortgage Cost per Year² Flow Flow
Payment³
+$(241) +$(192) -$697 $262 $505

## Slide 10
Documentation Required to Meet Criterion 5
The following documentation must be provided as evidence to verify that the municipality has met this criterion:
Stretch Energy Code
The municipality must provide documentation of the town meeting vote adopting 780 CMR 115.AA, the MA Board of Building Regulations and Standards (BBRS) Stretch Energy Code. The vote must include the effective date of the Stretch Energy Code.