Appendix 2

Tables 1-7

TABLE 1

Recommended Geometric Design Standards for Roadways

| DESIGN ELEMENTS | Ways | Minor Roadways | Major Roadways | Collector Roadways | Figure Reference |
| --- | --- | --- | --- | --- | --- |
| Roadway layout |  |  |  |  |  |
| Minimum right-of-way width | 40 feet | 50 feet | 50 feet | 50 feet | fig. 3 |
| Minimum Roadway width – not including berms | 20 feet | 22 feet | 22 feet | 22 feet | fig. 3 |
| Sidewalks (width) | n/a | 4 feet | 4 feet | 4 feet | fig. 9 |
| Clearance above grade |  |  |  |  |  |
| Horizontal Alignment |  |  |  |  |  |
| Minimum radius at street centerline | 150 feet | 150 feet | 300 feet | 400 feet | fig. 4 |
| Vertical Alignment |  |  |  |  |  |
| Clear sight distance from 4’-6”’ to 4” above pavement | 200 feet | 200 feet | 350 feet | 350 feet | fig. 2 |
| Minimum vertical curve | 100 Feet | 100 feet | 100 feet | 100 feet | fig. 2 |
| Grade |  |  |  |  |  |
| Maximum grade | 8% | 8% | 6% | 6% | fig. 2 |
| Minimum grade | 1% | 1% | 1% | 1% | fig. 2 |
| Maximum grade, within 30’ from intersection | 2% | 2% | 2% | 2% | fig. 2 |
| Intersection Standards |  |  |  |  |  |
| Minimum intersection angle | 70° | 70° | 85° | 85° | fig. 1 |
| Minimum centerline offset | 125 feet | 125 feet | 200 feet | 200 feet | fig. 4 |
| Minimum curb (or edge of roadway) radius | 15 feet | 15 feet | 30 feet | 30 feet | n/a |
| Required Cleared Area at Intersection | 100 feet | 100 feet | 150 feet | 150 feet | fig. 4 |
| Dead-end Street |  |  |  |  |  |
| Maximum length | 1,200 feet | 1,200 feet | Not allowable | Not allowable | fig. 1 |
| Minimum radius of circular turnaround, to curb or to edge of pavement | 45 feet | 45 feet | n/a | n/a | fig. 1 |
| Pavement and Storm Frequency Standards |  |  |  |  |  |
| Unpaved* | 6” T-Base 3” crushed Stone | n/a | n/a | n/a | fig. 3A |
| Pavement, compacted thickness | 3” total 2” binder 1” finish | 3” total 2” binder 1” finish | 4½” total 2½” binder 2” finish | 4½” total 2½” binder 2” finish | fig. 3 |
| Base, compacted thickness | 8” total 4” sub-base 4” base | 8” total 4” sub-base 4” base | 12” total 6” sub-base 6” base | 12” total 6” sub-base 6” base | fig. 3 |
| Storm frequency for drainage calculations | 25 years | 25 years | 25 years | 50 years |  |
| Storm frequency for cross culverts sizing | 50 years | 50 years | 50 years | 100 years |  |

n/a – Not applicable.

*Although unpaved roads may be accepted as access for no more than 5 lots or dwelling units under these regulations, they will not be considered for acceptance as a town road unless reconstructed.

TABLE 2

DENSE GRADED CRUSHED STONE BASE MATERIAL

| Sieve Size | Gradation - % Passing |
| --- | --- |
| 2" | 100 |
| 1½" | 70-100 |
| ¾" | 50-85 |
| No. 4 | 30-55 |
| No. 40 | 10-35 |
| No. 200 | 2-10 |

TABLE 3

RECLAIMED PAVEMENT BORROW MATERIAL FOR BASE COURSE

| Sieve Designation | Percent Passing |
| --- | --- |
| 3" | 100 |
| 1½" | 70-100 |
| ¾" | 50-85 |
| No. 4 | 30-60 |
| No. 50 | 8-24 |
| No. 200 | 0-10 |

TABLE 4

GRADATION FOR AGGREGATE IN BITUMINOUS

CONCRETE PAVEMENT TYPE I

| Sieve Size | Binder Course % Passing* | Finish Course % Passing* |
| --- | --- | --- |
| 7/8" | 100 |  |
| ¾" | 80-100 |  |
| ½" | 50-80 | 100 |
| 3/8" | 50-55 | 80-100 |
| No. 4 | 28-50 | 50-76 |
| No. 10 | 18-35 | 35-45 |
| No. 20 | 10-25 | 22-35 |
| No. 40 | 7-18 | 14-27 |
| No. 80 | 3-10 | 6-18 |
| No. 200 | 1-4 | 3-6 |

*by weight

Table 5 – Typical Parking Schedule

| Parking Requirements Generator | Quantity or Rated Capacity | Basis For Parking Calculation per Zoning By-law | Number of Spaces Required |
| --- | --- | --- | --- |
| Retail Space | 4,300 sq. ft. | One space per each 200 sf of floor area devoted to customer use | 22 |
| Restaurant | 59 seats | One space for each three units of rated capacity | 20 |
| Employees, maximum shift | 18 | 1 space for every 2 employees, max shift | 9 |
| TOTAL NUMBER OF SPACES REQUIRED | 51 |

Table 6 – Typical Zoning Compliance Table

| Zoning District: _____ |
| --- |
| Subject | Existing | Required | Proposed |
| Lot Area | 32,547 sq. ft. | 20,000 sq. ft. | 32,547 sq. ft. |
| Frontage | 112 ft. | 100 ft. | 112 ft. |
| Front Setback | 20 ft. | 25 ft. | 25 ft. |
| Side 1 Setback | 5ft. | 10 ft. | 62 ft. |
| Side 2 Setback | 20ft. | 10 ft. | 13 ft. |
| Rear Setback | 20 ft. | 10 ft. | 35 ft. |
| Minimum Front Parking Setback | 10 ft. | 15 ft. | 15 ft. |
| Minimum Side Parking Setback | 5 ft. | 5 ft. | 5 ft. |
| Minimum Rear Parking Setback | 5 ft. | 5 ft. | 5 ft. |
| Building Coverage | 43% | 50% max | 31% |
| Site Coverage | 78% | 80% max | 75.5% |
| Building Height | 22ft. | 30 ft. | 26 ft. |
| Interior Landscaping | 0% | 10% | 10.8% |
| Number of Parking Spaces | 17 | 21 | 21 |
| Driveway Width | 24 ft. | 30 ft. | 29 ft. |

Note: Add additional columns if the project involves more than one zone.  Table 6 serves as an example only of how a typical Zoning Compliance table should be organized on a site plan.  Please refer to the Town of Harwich Zoning By-law for the requirements for each zoning district.

Table 7 – Typical Planting Schedule

| Symbol | Quantity | Common Name | Type* | Size | Spacing | Comments |
| --- | --- | --- | --- | --- | --- | --- |
|  | 10 | Eastern Red Cedar | E, S | 3’ | 5’ O.C. | Parking screen |
|  | 5 | American Holly | E, T | 3’ | 6’ O.C. | Parking screen |
|  | 12 | Japanese Beach Rose | D, S | 3 gal | Random | Parking setback |
|  | 4 | Winterberry Holly | D, S | 3 gal | 1/island | Int landscaping |
|  | 4 | Green Ash | D, T | 8’ | 1/island | Int landscaping |
|  | 8 | Red Oak | D, T | 8’ | Random | Parking setback |
|  | 4 | Common Bayberry | D, S | 30” | Random | Parking setback |

*Types:	E = Evergreen     D = Deciduous     S = Shrub     T = Tree	Note: The above species are examples only of native plantings that generally require low maintenance and little or no fertilizers or pesticides.  Other species may be proposed.  It is Planning Board policy to encourage the use of native species to optimize planting survival and minimize the application of chemicals, which may pollute groundwater.

# Text boxes

64